## Slide 1: Instructor Materials Chapter 9: Laptops and Mobile Devices
IT Essentials v6.0
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 2: Instructor Materials - Chapter 9 Planning Guide
This PowerPoint is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide #10
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
ITE 6.0 Planning Guide
Chapter 9: Laptops and Mobile Devices
Notes: ITE 6.0 Planning Guide
Chapter 9: Laptops and Mobile Devices

## Slide 4: Chapter 9: Activities
What activities are associated with this chapter?
Page Number | Activity Type | Activity Name
9.1.1.6 | Lab | Research Docking Stations
9.2.1.3 | Interactive Activity (IA) | Match ACPI Standards
9.3.1.5 | Lab | Research Laptop RAM
9.3.2.3 | Lab | Research Laptop Batteries
9.3.2.5 | Lab | Research Laptop Screens
9.3.2.7 | Lab | Research Laptop Hard Drives
9.3.2.13 | Video | Replace Laptop Components
9.3.2.14 | Lab | Research Building a Specialized Laptop
9.4.1.6 | IA | Identify Connection Types
9.6.2.2 | Lab | Research Laptop Problems
9.6.2.3 | Lab | Gather Information from the Customer
9.6.2.4 | Lab | Investigate Support Websites
Notes: 4

## Slide 5: Chapter 9: Assessment
Students should complete Chapter 9, “Assessment” after completing Chapter 9.
Quizzes, labs, and other activities can be used to informally assess student progress.
Notes: 5

## Slide 6
Prior to teaching Chapter 9, the instructor should:
Complete Chapter 9, “Assessment.”
The goal of this chapter is to provide an overview of laptops and mobile devices and provide the basics of preventive maintenance and troubleshooting on those devices.
Ensure that students understand that, just like desktop computers, laptops and mobile devices require periodic maintenance.
Make sure students understand that while electronic components experience less wear than mechanical components, all components will eventually fail due to normal operation.
Students may be discouraged by the troubleshooting process at first; make sure they understand it must be practiced and that it will take some time before they become experts.
Chapter 9: Best Practices
Notes: 6

## Slide 7: Chapter 9: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the ITE Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the ITE Community in order to help other instructors.
Notes: 7

## Slide 8: Chapter 9: Topics in chapter that are not found in the CompTIA A+ 220-901 Certification
This slide lists content included in this chapter that is NOT listed in the CompTIA A+ 220-901 blueprint. Instructors could skip these sections; however, they should provide additional information and fundamental concepts to assist the student with the topic.
All content in Chapter 9 is aligned to the certification.
Notes: 8

## Slide 10: Chapter 9: Laptops and Mobile Devices
IT Essentials v6.0
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 11: Chapter 9 - Sections & Objectives
9.1 Laptop Components
  Explain the purpose and characteristics of laptops.
9.2 Laptop Configuration
  Explain how to configure laptop power settings and wireless settings.
9.3 Laptop Hardware and Component Installation and Configuration
  Explain how to remove and install laptop components.
9.4 Mobile Device Hardware Overview
  Explain the purpose and characteristics of mobile devices.
9.5 Common Preventive Maintenance Techniques for Laptops and Mobile Devices
  Explain how to perform common preventive maintenance techniques for laptops and mobile devices.
9.6 Basic Troubleshooting Process for Laptops and Mobile Devices
  Explain how to troubleshoot laptops and mobile devices.
9.6 Chapter Summary
Notes: 11

## Slide 12: 9.1 Laptop Components
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 13: Laptops and Mobile Devices Laptop Components
Features of Laptop Components
  External Features Unique to Laptops
    Battery, Security keyhole, Docking Connector
  Common Input Devices and LEDs in Laptops
    Touchpad, Pointing stick, Keyboard, Fingerprint readers, Microphone, Web camera, LED indicators
  Internal Components
    Motherboards, RAM (SODIMMs), CPUs, Storage
  Special Function Keys
    Display settings, Media options, Sleep states, WI-FI & Bluetooth functionality
  Docking Station vs. Port Replicator
    Both add ports to laptop. Docking Station adds the ability to connect to PCI cards, additional hard drives, and optical drives.
Notes: 9.1 – Laptop Components
9.1.1 – Features of Laptop Components

## Slide 14: Laptops and Mobile Devices Laptop Components
Laptop Displays
  LCD, LED, and OLED Displays
    2 types of LCD: Twisted Nematic (TN) and In-Plane Switching (IPS)
      TN: Offer high brightness, uses less power than IPS, inexpensive
      IPS: Better color reproduction and better viewing angles
    LEDs: Use less power and have longer lifespan
    OLED: Commonly used for mobile devices and digital cameras
  Backlights and Inverters
    LCD: Cold Cathode Fluorescent Lamp (CCFL) & Inverter
    LED: LED based backlights
  WI-FI Antenna Connectors
    Typically located above the screen
    Connects to wireless card
  Webcam and Microphone
    Built into most laptops today
Notes: 9.1 – Laptop Components
9.1.2 – Laptop Displays

## Slide 15: 9.2 Laptop Configuration
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 16: Laptops and Mobile Devices Laptop Configuration
Power Settings Configuration
  Power Management
    Advanced Configuration and Power Interface (ACPI) standards
      Creates a bridge between hardware and Operating System
      Provides power management schemes for better performance
      Standards: S0 – S5
  Managing ACPI Settings in the BIOS
  Managing Laptop Power Options
    Sleep
    Hibernate
    Shutdown
Notes: 9.2 – Laptop Configuration
9.2.1 – Power Settings Configuration

## Slide 17: Laptops and Mobile Devices Laptop Configuration
Wireless Configuration
  Bluetooth
    Personal Area Network (PAN)
    3 Classes: Most common is Class 2 with a range of approx. 33 feet
    4 Specifications: Version 4 is newest with more advanced capabilities
    Supports 128-bit encryption and PIN authentication
  Cellular WAN
    Tethering: Can be made using Wi-Fi, Bluetooth, or USB cable
    Laptops can have integrated cellular WAN capabilities.
  WI-FI
    Mini-PCI: older laptops, 124 pins, 802.11a, 802.11b, and 802.11g
    Mini-PCIe: Most common, 54 pins, all 802.11 standards
    PCI Express Micro: ½ size of Mini-PCIe, 54 pin, all 802.11 standards
Notes: 9.2 – Laptop Configuration
9.2.2 – Wireless Configuration

## Slide 18: 9.3 Laptop Hardware and Component Installation and Configuration
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 19: Laptops and Mobile Devices Laptop Hardware and Component Installation and Configuration
Expansion Slots
  Expansion Cards
    2 Models: ExpressCard/34 & ExpressCard/54
    Add functionality to laptop: Additional memory card reader, External hard drive access, TV tuner cards, USB and FireWire ports, Wi-Fi Connectivity
  Flash Memory
    External Flash Drive (SSD)
    Flash Cards (SD, SDHC)
  Smart Card Readers
    Contact – requires a physical connection to the card
    Contactless – works on a radio frequency
  SODIMM Memory
    32-bit: 72-pin and 100-pin
    64-bit: 144-pin, 200-pin, and 204-pin
Notes: 9.3 - Laptop Hardware and Component Installation and Configuration
9.3.1 - Expansion Slots

## Slide 20: Laptops and Mobile Devices Laptop Hardware and Component Installation and Configuration
Replacing Hardware Devices
  Overview of Hardware Replacement
    Customer-Replaceable Units (CRUs)
    Field-Replaceable Units (FRUs)
  Power
    Most batteries are CRU
    Signs Battery needs to be replaced: Does not hold charge, overheats, leaking
  Keyboard, Touchpad, and Screens
  Internal Storage Drive and Optical Drive
  Wireless Card
  Speakers
  CPU
  Motherboard
  Plastic Frames
Notes: 9.3 - Laptop Hardware and Component Installation and Configuration
9.3.2 - Replacing Hardware Devices

## Slide 21: 9.4 Mobile Device Hardware Overview
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 22: Laptops and Mobile Devices Mobile Device Hardware Overview
Mobile Device Hardware
  Mobile Device Parts
  Non-Upgradeable Hardware
  Touchscreens
    Recognize two or more points of contact
    Common Gestures: Swipe, Double touch, Long touch, Scroll, Pinch, Spread
  Solid State Drives
    Advantages: Power efficiency, Reliability, Lightweight, Compact, Performance, No noise
  Connection Types
    Wired: Micro/Mini USB, Lightning, Proprietary vendor specific ports
    Wireless: NFC, IR, Bluetooth
  Accessories
    External Battery
    Docking Station
    Portable Chargers
  Ear Buds
  Headsets
  Speakers
  Game Pad
  SD cards
  Credit Card Reader
Notes: 9.4 - Mobile Device Hardware Overview
9.4.1 – Mobile Device Hardware

## Slide 23: Laptops and Mobile Devices Mobile Device Hardware Overview
Other Mobile Devices
  Wearable Devices
    Smart Watches
    Fitness Monitors
    Smart Headsets
  Specialty Devices
    GPS Receiver
    Smart Cameras
    Electronic Readers
Notes: 9.4 - Mobile Device Hardware Overview
9.4.2 – Other Mobile Devices

## Slide 24: 9.5 Common Preventive Maintenance Techniques for Laptops and Mobile Devices
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 25: Laptops and Mobile Devices Common Preventive Maintenance Techniques for Laptops and Mobile Devices
Scheduled Maintenance for Laptops and Mobile Devices
  Scheduled Maintenance
    More exposure
    Laptops
      Cleaning
      Hard drive maintenance
      Software updates
    Mobile Devices
      Cleaning
      Backing up the data
      Updating the system and applications
Dirt and contamination
Spills
Wear and tear
Drops
Excessive heat & cold
Excessive moisture
Notes: 9.5 – Common Preventive Maintenance Techniques for Laptops and Mobile Devices
9.5.1 – Scheduled Maintenance for Laptops and Mobile Devices

## Slide 26: 9.6 Basic Troubleshooting Process for Laptops and Mobile Devices
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 27: Laptops and Mobile Devices Basic Troubleshooting Process for Laptops and Mobile Devices
Applying
  Identify the Problem
    Open-ended questions
    Closed-ended questions
  Establish a Theory of Probably Cause
  Test the Theory to Determine Cause
  Establish a Plan of Action to Resolve the Problem and Implement the Solution
  Verify Full System Functionality and Implement Preventive Measures
  Document Findings, Actions, and Outcomes
Common Problems and Solutions for Laptops and Mobile Devices
  Identify Common Problems and Solutions
Notes: 9.6 - Basic Troubleshooting Process for Laptops and Mobile Devices
9.6.1 – Applying
9.6.2 - Common Problems and Solutions for Laptops and Mobile Devices

## Slide 28: 9.7 Chapter Summary
Notes: Cisco Networking Academy Program
IT Essentials
Chapter 9: Laptops and Mobile Devices

## Slide 29: Chapter Summary Summary
This chapter discussed the features and functionality of laptops and mobile devices, as well as how to remove and install internal and external components. The following concepts from this chapter are important to remember:
Laptops and mobile devices are lightweight and can operate on battery power.
Laptops use the same types of ports as desktop computers so that peripheral devices can be interchangeable. Mobile devices can also use some of the same peripheral devices.
Essential input devices, such as a keyboard and track pad, are built into laptops to provide similar functionality as desktop computers. Some laptops and mobile devices use touchscreens as input devices.
The internal components of laptops are typically smaller than desktop components because they are designed to fit into compact spaces and conserve energy. The internal components of mobile devices are usually connected to the circuit board to keep the device compact and light weight.
Laptops feature function keys that can be pressed in combination with the Fn key. The functions performed by these keys are specific to the laptop model.
Docking stations and port replicators can increase the functionality of laptops by providing the same types of ports that are featured on desktop computers. Some mobile devices use docking station to charge or use peripheral devices.
Notes: 9.7.1 - Summary

## Slide 30: Chapter Summary Summary (Cont.)
Laptops and mobile devices most commonly feature LCD and LED monitors or touchscreens.
Backlights and inverters illuminate laptop displays.
The power settings of laptop batteries can be configured to ensure that power is used efficiently.
Laptops and mobile devices can feature a number of wireless technologies, including Bluetooth, Infrared, Wi-Fi and the ability to access Cellular WANs.
Laptops provide a number of expansion possibilities. Users can add memory to increase performance, make use of flash memory to increase storage capacity, or increase functionality by using expansion cards. Some mobile devices can add more storage capacity by upgrading or adding more flash memory, such as MicroSD cards.
Laptop components consist of CRUs and FRUs.
Laptop components should be cleaned regularly in order to extend the life of the laptop.
Notes: 9.7.1 - Summary

## Slide 33: Chapter 9 New Terms and Commands
acpi
airplane (phone mode)
backlight
ccfl
ddr
ddr2
ddr3
dimm
diode
displayports
emmc
esata
expresscard
firewire
ips
lcd
microsd
nfc
oled
touchscreen
passkey
phablet
sd
sdhc
smartwatch
sodimm
tethering
ultrabooks
wearable
Notes: New Terms and Commands